## Slide 1
ARDUINO BEGINNERS COURSE
Lesson 3
Arduino UNO Complete +
Introduction to the Breadboard
Student Notes | Ages 10–15 | ⚠️ Safety First!
Understanding before connecting — prevents short circuits!

## Slide 2
01
REMAINING ARDUINO UNO PARTS
Parts we complete today — you will use all of these in your projects:
🟢 Power LED (ON)
Green LED that lights up when the board has power. If OFF — board is not powered!
〜 PWM Pins (3,5,6,9,10,11)
Pins marked ~ can simulate analog output using Pulse Width Modulation. Used to dim LEDs and control motors.
📡 TX / RX Pins (0 & 1)
Serial communication. TX sends data, RX receives. Avoid for simple projects — shared with USB.
🔌 ICSP Headers
Used to program chips directly. ADVANCED — do not connect anything here for now.
📏 IOREF & AREF
Reference voltage pins used by advanced shields and sensors. Leave unconnected for beginner projects.

## Slide 3
02
PWM — PULSE WIDTH MODULATION
PWM lets Arduino simulate different voltage levels by switching pins ON and OFF very rapidly:
0% (OFF)
LED fully off
25% Duty
LED dim
50% Duty
LED half bright
75% Duty
LED bright
100% (ON)
LED fully on
💡 Code: analogWrite(9, 127) → sets pin 9 to ~50% brightness (value 0–255)

## Slide 4
03
WHAT IS A BREADBOARD?
A breadboard is a reusable, solderless board for building and testing circuits safely:
+ (5V — RED WIRE FROM ARDUINO)
– (GND — BLACK WIRE FROM ARDUINO)
Terminal Strip A
(Rows 1–30
A B C D E)
GAP
Terminal Strip B
(Rows 1–30
F G H I J)
+ (Red Rail)
⚡ Red rail — all holes connected → 5V
⚡ Blue rail — all holes connected → GND
🟢 Same row = connected internally
⚠️ Gap separates left and right sides
🟢 Rows are numbered 1 to 30 (or 60)

## Slide 5
04
HOW BREADBOARD ROWS WORK
This is the most important concept — understanding internal connections:
Row 1
A1
B1
C1
D1
E1
A1, B1, C1, D1, E1 all connected internally ✓
Row 2
A2
B2
C2
D2
E2
A2, B2, C2, D2, E2 all connected internally ✓
Row 3
A3
B3
C3
D3
E3
NOT connected to Row 1 or Row 2 ✗
⚡ KEY RULE:
Same ROW number = connected. Different ROW number = NOT connected. The gap in the middle separates left (A–E) from right (F–J).

## Slide 6
05
COMMON SHORT CIRCUIT MISTAKES
Learn these NOW — they protect your Arduino from permanent damage:
❌ 5V connected directly to GND
✅ Always have a component between 5V and GND
❌ No resistor with an LED
✅ Always use a 220Ω resistor in series with every LED
❌ Both LED legs in the same row
✅ Each component leg must go in a DIFFERENT row
❌ LED inserted backwards
✅ Long leg (+) toward positive. Short leg (–) toward GND
❌ Changing wires while powered
✅ ALWAYS disconnect power before modifying the circuit
🔑 Golden Rule: BUILD FIRST. CHECK. THEN POWER ON.

## Slide 7
06
YOUR FIRST SAFE CIRCUIT — LED ON BREADBOARD
1
Place Arduino UNO + Breadboard on Tinkercad canvas
2
RED wire: Arduino 5V → Breadboard + (red) rail
3
BLACK wire: Arduino GND → Breadboard – (blue) rail
4
Resistor (220Ω): legs in Row 10 and Row 14
5
LED: long leg in Row 14, short leg in Row 16
6
Wire from – rail to Row 16 (LED cathode to GND)
7
Wire from Arduino Pin 13 to Row 10 (to resistor)
8
CHECK everything — then START SIMULATION!

## Slide 8
07
PRE-POWER SAFETY CHECKLIST
Run through this checklist EVERY TIME before connecting power:
☐ Power is DISCONNECTED while building
☐ Every LED has a 220Ω resistor in series
☐ LED long leg faces positive (+), short leg faces GND (–)
☐ Each component leg is in a DIFFERENT breadboard row
☐ Red wire connects Arduino 5V to + power rail
☐ Black wire connects Arduino GND to – power rail
☐ No bare wire ends are touching each other
☐ Circuit has been checked from beginning to end
☐ NOW it is safe to connect power and simulate!

## Slide 9
Lesson 3 Complete!
You now know every Arduino UNO part
AND how to safely use a breadboard.
🔑 Remember: BUILD FIRST. CHECK. THEN POWER ON.
Next Lesson: Build your first LED blink circuit on a breadboard in Tinkercad! 🚀